产品规格承认书

Product Specification

产品名称/Product Name:       LAMP φ5mm产品

文件编号/Document Number: PDS- P0513A-KP-H3A4-I0

版 本 号/Version Number：           B0_________________

- 页    数/Page Number：           共 10 页______________

色 容 差/ SDCM :                    无_________________

- 机  差/Tolerence ：（√）无机差 （ ）有机差____________

产品应用/Product Application:__________________________

客户要求/Customer Requirement：1. ______________________

2.                             3. ______________________

| 源磊 Runlite | 客户 Customer 客户代码： |
| --- | --- |
| 制作 Prepared | 林跃敏 | 工程 Engineering |  |
| 审核 Checked | Fealty zhu | 品质 Quality |  |
| 批准 Approved |  | 批准 Approved |  |

注：此页和最后一页也为签核部分，请全部签核并盖章后回传到我司，谢谢。

LAMP φ5mm单芯系列规格书

LAMP φ5mm Single Chip Data Sheet

8.7mm长*5.0 mm宽                                8.7mm*5.0mm LAMP LED, Thickness.

角度：40°                                       View Angle:40°

包装：1000PCS一包                                Package：1000PCS/Packet

晶片材质：ALGaAs                                  Chip material: ALGaAs

胶体颜色：无色透明                                Lens color: water clean

工作温度：-40～80度                               Operating Temperature:-40～+80℃

低功率                                            Low Power Consumption

可做不同的种类.                                   Various Colors And Types Available.

胶水：环氧胶                                      Resin(Mold):Epoxy resin

反向电压5V                                        Reverse Voltage:5V

储存温度-40～+100度                               Storage Temperature:-40～+100℃

Note:

图中所有尺寸均以毫米为单位All dimensions are in millimeter

所有的标示尺寸仅供参考，除了有特别标注外，尺寸公差为±0.25 毫 米.

All dimensions for reference only, dimensions are in mm tolerance is ±0.25mm unless otherwise noted.

多胶不超过0.5 毫米. Burr around bottom of epoxy may be 0.5mm max.

● Applications /应用：

Infrared applied system / 红外应用系统

remote control / 遥控器

● 极限参数（温度=25℃）Absolute maximum ratings at Ta=25℃

| 项目 Item | 符号 Symbol | 极限参数 Absolute Maximum Rating | 单位 Unit |
| --- | --- | --- | --- |
| 正向电流 Forward Current | IF | 50 | mA |
| 正向脉冲电流 Pulse Forward Current | IFP | 200 | mA |
| 反向电压 Reverse Voltage | VR | 5 | V |
| 功耗 Power Dissipation | PD | 75 | mW |
| 操作温度 Operating Temperature | Topr | -40~80 | ℃ |
| 储存温度 Storage Temperature | Tstg | -30~100 | ℃ |

注: IFP 脉冲条件为脉冲宽度≤100 us和周期≤1%

Notes: IFP conditions—Pluse width ≤ 100 us and Duty ≤1%

● 光电参数（温度=25℃）Optical-Electrical Characteristics at Ta=25℃

| 参数名称 Parameter | 符号 Symbol | 数值 Value | 单位 Unit | 测试条件 Test condition |
| --- | --- | --- | --- | --- |
|  |  | Min. | Typ. | Max. |  |  |
| 发光强度 Radiant Intensity | Ie | - | 10 | - | mW/sr | IF=20mA |
|  |  | - | 28 | - | mW/sr | IF=50mA |
| 峰值波长 Peak Wavelength | λp | - | 940 | - | nm | IF=20mA |
| 半波宽 Spectral Bandwidth | △λ | - | 50 | - | nm | IF=20mA |
| 正向电压 Forward Voltage | VF | - | 1.20 | 1.50 | V | IF=20mA |
|  |  | - | 1.30 | 1.60 | V | IF=50mA |
| 反向电流 Reverse Current | IR | - | - | 10 | uA | VR=5V |
| 全视角 View Angle | 2θ1/2 | - | 40 | - | Deg | IF=20mA |

| 此项以客户下采购合同要求光电参数规格为准 |  |
| --- | --- |
| The customer requirements under the purchase contract photoelectric parameter specifications |
| Notes: 发光强度(Ie)±10% Radiant Intensity Tolerance ±10% |

| 焊接模式 Mode | Fixed form 固定形式 |
| --- | --- |
| Hand Soldering 手工焊接 | Temperature .at tip of iron 电烙铁温度 | 300℃Max.(30WMax.) 最高温度300℃（功率不超过30 瓦） |
|  | Soldering time 焊接时间 | 3 sec Max. 时间不超过3 秒 |
|  | Distance 焊接位置 | 3mm Min.(From solder joint to case) 大于3 毫米（从焊点到胶体） |
| DIP Soldering 锡炉焊接 | Preheat temperature 预热温度 | 100℃ Max. (60 sec Max.) 最高温度100℃（不超过60 秒） |
|  | Soldering temperature 浸焊温度 | 260℃ Max 最高260℃ |
|  | Soldering time 浸焊时间 | 3 sec Max. 不超过3 秒 |
|  | Distance 浸焊位置 | 2mm Min 大于2 毫米 |
| Wave Soldering 波峰焊接 | Preheat temperature 预热温度 | 100℃ Max. (60 sec Max.) 最高温度100℃（不超过60 秒） |
|  | Soldering temperature 浸焊温度 | 260℃ Max. 最高260℃ |
|  | Soldering time 焊接时间 | 5 sec Max. 不超过5 秒 |

● 典型光电特性曲线Typical Optical-Electrical Characteristics curves

环境参数Environment Parameter：温度Temperature=25℃， 湿度Humidity=60%

| 伏安特性曲线 Forward Current vs Forward Voltage | 相对光强与环境温度曲线 Relative Luminous Intensity vs. Ambient Temperature |
| --- | --- |
| 光谱特性曲线图 Relative Spectral Distribution | 光强分布与角度 Relative Intensity vs.Radiation Angle |

● 信赖性测试项目及标准  Test items and results of reliability

| 测试项目 Test Item | 测试条件 Test Conditions | 持续周期 Duration/Cycle | 数量 Quantity | 接收/拒收 Ac/Re |
| --- | --- | --- | --- | --- |
| 温度循环 Temperature | -40℃ 30min ↑↓25℃(2min) 100℃ 30min | 循环100次 100 times | 22pcs | 0/1 |
| 冷热冲击 Thermal Shock | -40℃ 30min ↑↓ 5sec 100℃ 30min | 循环100次 100 times | 22pcs | 0/1 |
| 高温储存 High Temperature Storage | Ta=100℃ | 1000小时 1000 hours | 22pcs | 0/1 |
| 高温高湿 Humidity Heat Storage | Ta=85℃ RH=85% | 1000小时 1000 hours | 22pcs | 0/1 |
| 低温储存 Low Temperatue Storage | Ta=-40℃ | 1000小时 1000 hours | 22pcs | 0/1 |
| 常温老化 Room Temperatue Test | Ta=25℃ IF=20mA | 1000小时 1000 hours | 22pcs | 0/1 |
| 高温高湿老化 High Humidity Heat Test | 60℃ RH=90% IF=20mA | 1000小时 1000 hours | 22pcs | 0/1 |
| 低温老化 Low Temperature Test | Ta=-40℃ IF=20mA | 1000小时 1000 hours | 22pcs | 0/1 |

- 失效判断标准 Criteria for judging the Damage

| 项目 Item | 符号 Symbol | 条件 Condition | 失效判断标准 Criteria for Judgement |
| --- | --- | --- | --- |
|  |  |  | 下限 MIN | 上限 MAX |
| 顺向电压 Forward Voltage | VF | IF=20mA | --- | USL×1.1 |
| 反向电流 Reverse Current | IR | IF=5V | --- | 10uA |
| 发光强度 Radiant Intensity | Ie | IF=20mA | LSL×0.7 | --- |

备注[Note]:

*1 USL:标准上限值        Uper Specification Level

*2 LSL:标准下限值        Lower Specification Level

● 包装规格 Packaging

●注意事項/Caution

1、 After open the package, the LED should be kept at 25oC, 65 % RH environment or less.

打开包装后请在温度25±3 oC湿度65±5%的环境下使用。

2、10℃-26℃，40%-65% RH. Store the product in sealed package.

湿度10℃～26℃，湿度40%～65%，包装袋密封保存.

3、The LED should be soldered within 48 hours ( 2 days ) after opening the package.

打开包裝后请在24小时内作焊接.

4、It is recommended to use a wrist band or an antistatic glove when handling the LEDs. Operation tables must beearthed, and in order to avoid the oxidizing of the Lamp leads make sure you will seal the package soon after it isopened.

接触LED 时需戴手套或手指套，工作台面要接地，包装袋开口后及时封口,防止脚位氧化

5、The LAMP  LED is an ESD sensitive device. All the equipment and machine must be  properly grounded.

LED是静电敏感器件，使用时所有设备、机械都需有适当的接地导电措施。

6、when make use of it,please use static-free container,operator showld ware antistatic clothes and rope-satic-ring

also should make effective ground.

使用时请使用防静电的盛裝容器，作业人员应穿著防静电服装及佩带有绳之静电环并作有效接地。

7、Damaged device will appear some symptoms,lower forward voltage,higher leak current,or even short curcuit

受静电与突波破坏之LED的电性特性上，会有明显的漏电流，或驱动电压明显变低，甚至是短路现象。

8、when shaped pin should used tong or by professional staff ,keep 3mm at least between lens and bend pin, the pin should been shaped before soldering..

引脚成形必须使用夹具或由专业人员来完成，离胶体最少3mm才能弯折引脚，并请在焊接前完成引脚成形。

9、the pin can’t  not be press in high temperature, cut pin in room temperature because in high temperature LED may fail

高温时，不可对引脚施压，请在室温时裁切引脚，高温时裁切可能会造成LED失效。

10、after shape ,pin space should keep in line with the PCB board space

引脚成形后必须保证引脚间距和线路板上一致。

11、LED is one-way continuity, please check electrode before mount, if amount wrong ,the LED chip will damage or fail when LED applied voltage

单向导通性，安裝前确认极性，若裝反，在施加电压时容易造成LED晶片损伤或失效。

12、ordinary our LED the long pin is anode ,shot pin is cathode, lens without gap is anode ,with gap is cathode.unless other special require and note

通常在无特別要求或提示下，我们提供的LAMP LED的长脚为正极，短脚为负极。胶体无缺口的一端为正极，有缺口的一端为负极。

13、please design the PCB board to keep a distance between LED and other emit heat component

线路设计时，请不要將LED与发热元件靠得过近。

14、strongly recommend design the board according setting current other than setting voltage .if you are really need setting voltage type please consider there may cause influence arise by difference voltage of difference LED

电路设计上，建议以定电路设计，若为定电压设计，请考虑LED之间不同正向电压所可能造成之影响。

15、the outer voltage change will bring the current index change .unsuitable design and current control,easy cause LED fail .for example excess current will cause LED life short or even burn down , too little electricity will cause lacking light

LED之外加电压变化，会造成电流指数级变化，不当之设计与电流控制，易造成LED失效，如电流过大引起寿命问题甚至烧毁，

电流过小引起亮度不足。

16、If you need make difference BIN LED in the one module .please confirm whether it can meet the electric and optics characteristic require such as the current balance, emitting and brightness consistency.

不同BIN号之LED需安裝在同一个组件时，请先确认是否可满足相关电流及光学之特性要求，如电流是否均衡，光色、亮度的一致性等。

17、To protect your eyes, please don’t watch the product directly when the LEDs lighten.

请不要直视点亮的LED，以免伤害眼睛.

18、It’s unsuitable for circumfluence soldering

本產品不適合作回流焊接。

19、ferrochromium soldering :power keep no more than 30W,tip temperature should not pass 280 oC,soldering time within 3 second, welding position and lens should keep 3mm distance at least

烙铁焊接时烙铁功率不要超過30W，尖端溫度不要超過280 oC，焊接时间不要超过3秒，焊接位置最少与胶体保持3mm距离。

20、wave-soldering: temperature should not pass 265 oC, soldering time within 5 second, welding position and lens should keep 3mm distance at least

波峰焊接時温度不超過265 oC，焊接时间不要超過5秒，焊接位置最少与胶体保持3mm距離。

21、After soldering the LED should keep out off any shake or outer force before it come to normal tempreture

在焊接温度回到正常以前，必须避免使LED受到任何震动或外力。

| 源磊/Runlite | 客户/Customer |
| --- | --- |
| 制作/Prepared | 林跃敏 | 工程/Engineering |  |
| 审核/Checked | Fealty zhu | 品质/Quality |  |
| 批准/Approved |  | 批准/Approved |  |

# Text boxes

关注请扫一扫

● 特性 Features

● 产品编码解说 Product Definition Code

● 封装尺寸 Dimension

● Recommended soldering conditions 推荐焊接条件